## Slide 1: CS2115 Computer Organization 2023/2024 Sem A
Chapter 2: Number Systems
Dr. Nan Guan
Department of Computer Science
City University of Hong Kong

## Slide 2: Outline
Decimal, Binary, Octal, Hexadecimal Systems
  Conversion between different systems
  Arithmetic
Signed Number Representation
  Sign Magnitude Number
  Two’s Complement
Floating-point Number
BCD, ASCII, Gray …
Notes: We will talk about

## Slide 3: Outline
Decimal, Binary, Octal, Hexadecimal Systems
  Conversion between different systems
  Arithmetic
Signed Number Representation
  Sign Magnitude Number
  Two’s Complement
Floating-point Number
BCD, ASCII, Gray

## Slide 4: Decimal System
972.5 = 9×102 + 7×101 + 2×100 + 5×10-1
10
radix
R
Radix-R System
generalize
Radix-10 System

## Slide 5: Binary, Octal and Hexadecimal
Binary system (Radix-2)
Octal system (Radix-8)
Hexadecimal system (Radix-16)
2
12.125 = (14.1)8
12.125 = 1×81+4×80+1×8-1
12.125 = (1100.001)2
12.125 = 1×23+1×22+0×21+0×20+0×2-1+0×2-2+1×2-3
8
16
12.125 = (C.2)16
12.125 = C×160+2×16-1

## Slide 6: Binary  Octal  Hexadecimal

## Slide 7: Binary  Octal  Hexadecimal
10110011101.1011001
Octal
Hexadecimal
5 9 D . B 2
Binary
2 6 3 5 . 5 4 4
10110011101.1011001
Binary
00
0
0
0

## Slide 8: Conversion to Decimal
  (10101)2 = (1×24+ 0×23+1×22+ 0×21+1×20)10 = (21)10
  (1276)8 = (1×83+2×82+7×81+6×80)10 = (702)10
  (9DF8)16 = (9×163+D×162+F×161+8×160)10 = (40440)10
  (101.11)2 = (1×22+1×20+1×2-1+1×2-2)10 = (4+1+0.5+0.25)10 =(5.75)10
  (8A.E2)16 = (8×161+A×160+E×16-1+8×16-2)10
  = (128 + 10 + 14/16 + 8/256)10
  = (138.90625)10

## Slide 9: Conversion from Decimal
For integers: Radix divide method
(12)10 = ( ? )2
(12)10 = ( 1100 )2
(1582)10 = ( ? )16
(1582)10 = ( 62E )16

## Slide 10: Conversion from Decimal
For the fractional part: Radix multiply method
(0.72)10 = ( 0.10111 … )2
0.72×2 = 1.44
0.44×2 = 0.88
0.88×2 = 1.76
0.76×2 = 1.52
0.52×2 = 1.04
…
(0.72)10 = ( ? )2
(0.65)10 = ( ? )16
0.65×16 = 10.4
0.4×16 = 6.4
0.4×16 = 6.4
…
(0.65)10 = ( 0.A666 … )16

## Slide 11: Arithmetic
Direct computation:
  Following essentially the same rule as in decimal, with a different radix
1001
1101
+
0
1
1001
1101
+
10
1
1001
1101
+
110
1001
1101
+
10110
(1001)2+ (1101)2
(8B)16 × (3)16
8B
3
×
1
2
8B
3
×
1A1
2
Notes: We can also do

## Slide 12: Arithmetic
Indirect computation
  First convert everything to decimal, then compute, finally convert back
(1001)2+ (1101)2
(9)10+ (13)10
(22)10
(11010)2
(8B)16 × (3)16
(417)10
(1A1)16
(139)10 × (3)16

## Slide 13: Outline
Decimal, Binary, Octal, Hexadecimal Systems
  Conversion between different systems
  Arithmetic
Signed Number Representation
  Sign Magnitude Number
  Two’s Complement
Floating-point Number
BCD, ASCII, Gray

## Slide 14: Sign Magnitude Numbers
Naïve representation: the leftmost digit represents sign (sign digit), the remailing represents the absolute value
  sign digit =0  positive; sign digit = 1  negative
Drawbacks
  Addition/subtraction need to consider different cases of different signs
  Complicate circuit and more computation effort
  Rarely used in practice
sign
magnitude

## Slide 15: 2’s Complement
Rules:
  Positive numbers are represented in the same way as in sign magnitude numbers
  Negative numbers are represented as the complement of positive numbers
    Complement: change 1 to 0, change 0 to 1

## Slide 16: 2’s Complement
Consider a 8-bit binary system
  Cut the number system in half
  Use 00000001 – 01111111 to indicate positive numbers
  Use 10000000 – 11111111 to indicate negative numbers
01111111
01111110
01111101
00000001
00000000
11111111
11111110
10000001
10000000
pos(+)
neg(-)
+127
+126
+125
+1
0
-1
-2
-127
-128

## Slide 17: Sign Bit
The most significant bit (MSB) of the binary numbers is the signed bit
  The MSB is (0) for all positive numbers
    Except 00000000
  The MSB is (1) for all negative numbers
  Similar to sign magnitude numbers, this allows you to instantly determine whether a number is positive or negative
01111111
01111110
01111101
00000001
00000000
11111111
11111110
10000001
10000000
pos(+)
neg(-)
+127
+126
+125
+1
0
-1
-2
-127
-128

## Slide 18: 2’s Complement Process
To calculate the representation of a negative number – using 2’s Complement Process
  First, complement all of the digits in a number.
  Second, add 1.

## Slide 19: 2’s Complement Process
Example #1
Complement Digits
Add 1
5 = 00000101
-5 = 11111011

11111010
+1
Complement Digits
Add 1
Example #2
-13 = 11110011
13 = 00001101

00001100
+1

## Slide 20: 2’s Complement Arithmetic
Use the 2’s complement process to add the following numbers
9
+ (-5)
4
(-9)
+ 5
- 4
(-9)
+ (-5)
- 14
9
+ 5
14
POS
+ POS
POS

POS
+ NEG
POS

NEG
+ POS
NEG

NEG
+ NEG
NEG


## Slide 21: POS + POS → POS Answer
If no 2’s complement is needed, use regular binary addition.
00001001
9
+ 5
14


00001110
00000101

+

## Slide 22: POS + NEG → POS Answer
Take the 2’s complement of the negative number and use regular binary addition.
00001001
9
+ (-5)
4


11111011
+
00000101

11111010
+1
11111011
2’s
Complement
Process
1]00000100
8th Bit = 0: Answer is Positive
Disregard 9th Bit

## Slide 23: POS + NEG → NEG Answer
Take the 2’s complement of the negative number and use regular binary addition.
11110111
(-9)
+ 5
-4


00000101
+
00001001

11110110
+1
11110111
2’s
Complement
Process
11111100
8th Bit = 1: Answer is Negative
11111100

00000011
+1
00000100
To Check:
Perform 2’s
Complement
On Answer

## Slide 24: NEG + NEG → NEG Answer
Take the 2’s complement of both negative numbers and use regular binary addition.
11110111
(-9)
+ (-5)
-14


11111011

+
2’s Complement
Numbers, See
Conversion Process
In Previous Slides
1]11110010
8th Bit = 1: Answer is Negative
Disregard 9th Bit
11110010

00001101
+1
00001110
To Check:
Perform 2’s
Complement
On Answer

## Slide 25: Outline
Decimal, Binary, Octal, Hexadecimal Systems
  Conversion between different systems
  Arithmetic
Signed Number Representation
  Sign Magnitude Number
  Two’s Complement
Floating-point Number
BCD, ASCII, Gray

## Slide 26: Binary with Fractional Part
Recall that in binary number system
  (1001.1010)2 = 23 + 20 +2-1 + 2-3 =9.625
If we fix the position of the point
    We are not able to represent small numbers with high precision
    We are not able to represent large numbers
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Point is here
Point is here

## Slide 27: Floating-Point Numbers
32-bit Binary Floating-Point Numbers
value = (+/- Significand × 2E’)
  Sign bit: 0positive; 1negative
  Biased Exponent (E)
    Biased exponent E = real exponent value E’ + bias
    bias=2K-1 - 1, K=8 (8-bits of exponent), bias = 127
  Significand
    Normalized number: represent 1.xxx
    The most significant digit is always 1, so we do not need to store this information
    Thus, 23-bit is used to store 24-bit significand

## Slide 28: Floating-Point Numbers
32-bit Binary Floating-Point Numbers
value = (+/- Significand × 2E’)
  Sign bit: 0positive; 1negative
  Biased Exponent (E)
    Biased exponent E = real exponent value E’ + bias
    bias=2K-1 - 1, K=8 (8-bits of exponent), bias = 127
  Significand
    Normalized number: represent 1.xxx
    The most significant digit is always 1, so we do not need to store this information.
    Thus, 23-bit is used to store 24-bit significand
1
10000100
10100000000000000000000
negative
Biased exponent E = 132
Real exponent value E’ = 132 – 127 = 5
Significand = 1 + 0.101000... (binary)
= 1 + 0. 625 (decimal)
So the value of the number is
-1.625 × 25

## Slide 29: Outline
Decimal, Binary, Octal, Hexadecimal Systems
  Conversion between different systems
  Arithmetic
Signed Number Representation
  Sign Magnitude Number
  Two’s Complement
Floating-point Number
BCD, ASCII, Gray

## Slide 30: BCD: Binary-Coded Decimal
4-bit binary form to encode ten numbers from 0 to 9

## Slide 31: BCD: Binary-Coded Decimal
4-bit binary form to encode ten numbers from 0 to 9

## Slide 32: BCD: Binary-Coded Decimal
4-bit binary form to encode ten numbers from 0 to 9

## Slide 33: BCD: Binary-Coded Decimal
4-bit binary form to encode ten numbers from 0 to 9
137
10001001
0001 0011 0111

## Slide 34: ASCII Code
ASCII: American Standard Code for Information Interchange
ASCII encodes 128 specified characters into 7-bit integers

## Slide 35: Gray Code
An encoding of numbers so that adjacent numbers have a single digit differing by 1